## Slide 1: Calculating the resistance of a bulb
A filament bulb has a current of 5 A running through it, with a potential difference of 50 V across it.
What is the resistance of the filament in the bulb?
V = IR
R = V
I
= 50 V
5 A
= 10 

## Slide 2: P6 – Electricity for Gadgets
Lesson 3 – Resistors in series
Learning aim: Demonstrate an understanding of how resistors work in series circuits

## Slide 3
Learning Objectives
Success Criteria
Understand how potential dividers work.
Understand how to add resistors in series.
Calculate the output from a potential divider.
Recall the properties of potential dividers. (Grade E-D)
Use Rt = R1 + R2 to find the total voltage of resistors in series. (Grade E-D)
Explain how combinations of fixed and variable resistors can be used in potential divider circuits. (Grade C)
Calculate Vout for simple ratios of resistors.(HT) (Grade C-A)
Explain how a Vout with adjustable threshold can be achieved. (Grade C-A)

## Slide 4: Resistors in series
4 
2 
Total resistance = R1 + R2
What is the total resistance for this circuit?
Total resistance
= R1 + R2
= 4  + 2 
= 6 
When resistors are connected in series, the total resistance can be calculated using:

## Slide 5: Resistors in series
What is the total resistance for this circuit?
Total resistance = R1 + R2
= 6  + 34 
= 40 
6 
34 

## Slide 6: Copy the diagram and answer the questions
V
A
What is the resistance across this bulb?
Assuming all the bulbs are the same what is the total resistance in this circuit?
Voltmeter reads 10V
Ammeter reads 2A
LD

## Slide 7: Experiment - P6b 01 (part a)
Using a variable resistor as a potential divider.
At the end of this experiment you should be able to produce a definition for a potential divider

## Slide 8: Potential Dividers - Theory
0V
VIN
VOUT
0V
R1
R2
(R1 + R2)
VIN x
(R2)
VOUT
The Potential Divider equation:
Potential divider circuits allow us to obtain a required output voltage by ‘tapping off’ part of the input voltage

## Slide 9
R1
R2
V1
V2
V
V does not change
V = V1 + V2
The two resistors are dividing up the potential (or voltage) - (the Potential Divider)

## Slide 10: What happens if:
R1 increases and R2 is unchanged?
R1 decreases and R2 remains the same?
The values of both R1 and R2 are doubled?
The values of both R1 and R2 are halved?
The supply voltage V is trebled?
V1
V2
V
x 3
x 3
3V
V
V
V
V
V1
V1
V2
V2

## Slide 11
Uses of the potential divider
To supply a variable voltage
To make an input sensor from other components - many detectors will switch on as a voltage goes above or below a certain threshold (such as in a thermostat).

## Slide 12: Practical P6b01(part b)
I can design and construct a potential divider circuit to achieve a given output pd.
Equipment available: variety of resistors , leads, batteries, voltmeters.
HT

## Slide 13: Some example questions
0V
12V
VOUT
0V
100 
100 
0V
1.5V
VOUT
0V
50 
45 
0V
50V
VOUT
0V
10 
75 
0V
3V
VOUT
0V
75 
25 
HT

## Slide 14: Answers
A. 6V B. 44.12V
C. 0.75V D. 0.71V
HT

## Slide 15: To do
Complete the worksheet P6b01
Q2. Resistors in series
Then try – Q3a-c as well
Notes: Q3 for HT
WS could be for plenary LD. Or draw a potential divider circuit on white boards

## Slide 16: WS Answers
Q2a 6 V • Q2b 8 V • Q2c 6 V • Q2d 4  and 12  in series then take output from 4  • Q3a 6 V • Q3b 1000  • Q3c 4.5 V

## Slide 17: Plenary
VIN (V) | R1 (Ω) | R2 (Ω) | VOUT (V)
6 | 600 | 400 | 
40 | 9000 | 15 000 | 
 | 40 | 120 | 18
12 |  | 1000 | 3
Copy and complete the table, for the circuit below.
Give two ways in which a variable output can be obtained without setting up a new circuit each time.
HT
Notes: LD draw a potential divider circuit on white boards that includes a variable resistor

## Slide 18: Plenary answers
Replace R1 with a variable resistor; replace R2 with a variable resistor
VIN (V) | R1 (Ω) | R2 (Ω) | VOUT (V)
6 | 600 | 400 | 2.4
40 | 9000 | 15 000 | 25.0
24 | 40 | 120 | 18.0
12 | 3000 | 1000 | 3.0
HT

## Slide 19
Learning Objectives
Success Criteria
Understand how potential dividers work.
Understand how to add resistors in series.
Calculate the output from a potential divider.
Recall the properties of potential dividers. (Grade E-D)
Use Rt = R1 + R2 to find the total voltage of resistors in series. (Grade E-D)
Explain how combinations of fixed and variable resistors can be used in potential divider circuits. (Grade C)
Calculate Vout for simple ratios of resistors.(HT) (Grade C-A)
Explain how a Vout with adjustable threshold can be achieved. (Grade C-A)

## Slide 20: PC research task
http://www.bbc.co.uk/schools/gcsebitesize/science/triple_ocr_gateway/electricity_for_gadgets/sharing/revision/1/